## Slide 1
18.06.2015
New Interconnection Agreement between
FGSZ Ltd. and Ukrtransgaz

## Slide 2: An ascending path with 70 years’ experience
1975: Connecting to the Soviet natural gas transmission network with a pipeline DN800
1986: New DN1400 pipeline between Beregovo and Ukrainian-Hungarian border
1986: Old DN800 pipeline between Beregovo and Ukrainian-Hungarian border is out order
1990: New DN800 pipeline between Ukrainian-Hungarian border and Beregdaróc
2008: New DN1400 pipeline between Ukrainian-Hungarian border and Beregdaróc
2013: The DN800 pipeline section between Beregovo and Ukrainian-Hungarian border reopened, the transmission started to Ukraine on pipeline DN800 Beregdaróc-Beregovo
2015: New Interconnection Agreement between FGSZ Ltd. and Ukrtransgaz
2013
2015
1975
Connecting to the
Soviet Union
Transmission to
Ukraine started
1986
2008

## Slide 3: Before new Interconnection Agreement
There were two separate physical points and separate Agreements accordingly:
1. Gas flow direction from Ukraine to Hungary at Beregovo 1400 (UA -> HU)
a.) Dispatching Agreement
b.) Technical Agreement
2. Gas flow direction from Hungary to Ukraine at Beregdaróc 800 (HU -> UA)
a.) Technical Agreement – fix term contract, with interruptible capacity only

## Slide 4: Natural gas transmission between Ukraine and Hungary
M
M
Beregovo

## Slide 5: After new Interconnection Agreement
There are two separate physical points, but in one Agreement (IA):
Beregdaróc 1400
UA HU
Beregdaróc 800
HU UA
Capacity | Mm3/d (0 °C) | Mm3/d (15 °C) | GWh/d (25/0 °C) | Mm3/d (0 °C) | m3/d (15 °C) | GWh/d (15 °C)
 | Firm |  |  | Interruptible |  | 
Beregovo 1400 (UA>HU) | 53,35 | 56,3 | 605,28 | 14,42 | 15, 22 | 163,57
Beregdaróc 800 (UA>HU) | 0 | 0 | 0 | 15,92 | 16,80 | 181,02

## Slide 6: Requirements of CAM NC
Article 10 of Network Code on Capacity Allocation Mechanism
Applied capacity unit: The capacity offered shall be expressed in energy units per unit of time. The following units shall be used: kWh/h or kWh/d. In case of kWh/d a flat flow rate over the gas day is assumed.
Article 2 of ACER Framework Guidelines on Capacity Allocation Mechanism for the European Gas Transmission Network
The offer and use of separate capacity for transit purposes shall be forbidden. That means that capacity used for transit purposes by shippers shall not be treated differently than capacity used for domestic purposes.
Commission Decision of 10 November 2010 amending Chapter 3 of Annex I to Regulation (EC) No 715/2009 of European Parliament and the Council on conditions for access to natural gas transmission networks, 3.1.1 (1) f. point
(f) in consistent units, in particular kWh (with a combustion reference temperature of 298,15 K) shall be the unit for energy content and m3 (at 273,15 K and 1,01325 bar) shall be the unit for volume. The constant conversion factor to energy content shall be provided. In addition to the format above, publication in other units is also possible;
Article 3 of ACER Framework Guidelines on Interoperability Rules for European Gas Transmission Networks, Scoping Document 3. point
“The Framework Guideline should apply on the interconnection points between adjacent entry/exit systems (so not only on cross-border points) and on all other entry and exit points of those entry/exit systems (e.g. linked
to storage, LNG, production facilities and end consumers including these exit points which are connected to distribution systems) where gas can enter or exit the system.”
Notes: Network Code on Capacity Allocation Mechanism 10. point
(http://www.entsog.eu/public/uploads/files/publications/CAM%20Network%20Code/2013/EC_131014_CAM%20NC_Regulation%20984-2013.pdf)
  Applied capacity unit: The capacity offered shall be expressed in energy units per unit of time. The following units shall be used: kWh/h or kWh/d. In case of kWh/d a flat flow rate over the gas day is assumed.
ACER Framework guidelines on Capacity Allocation Mechanism for the European Gas Transmission Network 2. point
Commissions Decision of 10 November 2010 amending Chapter 3 of Annex I to Regulation (EC) No 715/2009 of European Parliament and the Council on conditions for access to natural gas transmission networks, 3.1.1 (1) point
ACER Framework Guidelines on Interoperability Rules for European Gas Transmission Networks, Scoping Document 3. point

## Slide 7: Why do we need an INT NC?
Network Users while delivering across different systems, would like to be sure that:
  Their nominated volumes shall be delivered.
  No quality issues shall be raised.
  Same procedures shall be followed by both up- and downstream TSOs.
  Communication and procedural rules shall be clear and common.
Harmonisation
Removal of barriers

## Slide 8: Process of Implementation INT NC
Development of the INT NC
ACER’s Reasoned Opinion
Implementation
Comitology
Develop Framework Guidelines
    July 2012
    Sep 2012-Sep 2013
    Dec 2013
    Nov 2014
    May 2015–May 2016

## Slide 9: (EU) 2015/703 - Interoperability Network Code (INT NC)
Article 3 General provisions
Adjacent transmission system operators shall ensure that at least the following terms and conditions detailed in Articles 6 to 12 are covered by an interconnection agreement in respect of each interconnection point:
rules for flow control;
measurement principles for gas quantities and quality;
rules for the matching process;
rules for the allocation of gas quantities;
communication procedures in case of exceptional events;
settlement of disputes arising from interconnection agreements;
amendment process for the interconnection agreement.
Notes: Network Code on Capacity Allocation Mechanism 10. point
(http://www.entsog.eu/public/uploads/files/publications/CAM%20Network%20Code/2013/EC_131014_CAM%20NC_Regulation%20984-2013.pdf)
  Applied capacity unit: The capacity offered shall be expressed in energy units per unit of time. The following units shall be used: kWh/h or kWh/d. In case of kWh/d a flat flow rate over the gas day is assumed.
ACER Framework guidelines on Capacity Allocation Mechanism for the European Gas Transmission Network 2. point
Commissions Decision of 10 November 2010 amending Chapter 3 of Annex I to Regulation (EC) No 715/2009 of European Parliament and the Council on conditions for access to natural gas transmission networks, 3.1.1 (1) point
ACER Framework Guidelines on Interoperability Rules for European Gas Transmission Networks, Scoping Document 3. point

## Slide 10: (EU) 2015/703 - Interoperability Network Code (INT NC)
    By 30 June 2015
    31 August 2015
    31 October 2015
    31 December 2015
Article 5 Interconnection agreement template
Any national regulatory authority may provide an opinion on the compliance of the template with national law to the Agency
The Agency having due regard to the opinions of the national regulatory authorities shall then provide its opinion on the ENTSOG template
After taking into account the opinion provided by the Agency, ENTSOG shall publish on its website the final template
ENTSOG shall develop and publish a draft interconnection agreement template covering the default terms and conditions
Notes: Network Code on Capacity Allocation Mechanism 10. point
(http://www.entsog.eu/public/uploads/files/publications/CAM%20Network%20Code/2013/EC_131014_CAM%20NC_Regulation%20984-2013.pdf)
  Applied capacity unit: The capacity offered shall be expressed in energy units per unit of time. The following units shall be used: kWh/h or kWh/d. In case of kWh/d a flat flow rate over the gas day is assumed.
ACER Framework guidelines on Capacity Allocation Mechanism for the European Gas Transmission Network 2. point
Commissions Decision of 10 November 2010 amending Chapter 3 of Annex I to Regulation (EC) No 715/2009 of European Parliament and the Council on conditions for access to natural gas transmission networks, 3.1.1 (1) point
ACER Framework Guidelines on Interoperability Rules for European Gas Transmission Networks, Scoping Document 3. point

## Slide 11: INT NC - ENTSOG template - FGSZ-UKRTR IA
INT NC | ENTSOG template (draft) | FGSZ – UKRTRANSGAZ IA
Article 6 - Rules for flow control |  | 
(1) a) Controllable, accurate, predictable, efficient gas flow across interconnection point | Article 2. 1.1 point | Nomination by hourly basis
Minimise steering differences | Article 2. 1.2 point | Article 5: „The Operator of the relevant measuring station shall carry out gas flow control to ensure that the balance of the sum of all confirmed nominations and the total measured gas quantity is at every moment as close to zero as possible.”
(1) b) Gas flow control, at all IP, hourly data |  | Nomination by hourly basis
(1) c) Designate the responsible TSO | Article 2. 1.3 point | Article 6: UA>HU: Ukrtransgaz Article 6: HU>UA: FGSZ

## Slide 12: INT NC - ENTSOG template - FGSZ-UKRTR IA
INT NC | ENTSOG template (draft) | FGSZ – UKRTRANSGAZ IA
Article 7 – Measurement principle |  | 
1. a) applicable measurement standards | Article 3: 3.1. and Annex | Annex 8-9-10. EN1776
1. b) TSO responsible for the installation, operation and maintenance of the measurement equipment | Article 3: 3.1. | Beregovo – Ukrtransgaz Beregdaróc controll DN1400 – FGSZ Beregdaróc DN800 – FGSZ
2. The installation, operation and maintenance of measurement equipment at an interconnection point shall take into account the technical requirements imposed by national regulations on the adjacent TSO. |  | 

## Slide 13: INT NC - ENTSOG template - FGSZ-UKRTR IA
INT NC | ENTSOG template (draft) | FGSZ – UKRTRANSGAZ IA
Article 8 – Rules for matching process |  | 
(1) a) rules detailing the matching process | 4.2. | 7.2. Matching process (in KWh, hourly basis, lesser rule, separate on DN800 and DN1400)
(2) Nomination, renomination | 4.2. | 7.3. Renominations
(3) Temporary reduction of capacity | 4.2. | 7.5. Reductions and interruptions
(4) Data exchange for the matching process | 4.2. | Sent by written notice
(5) Application of „Lesser Rule” | 4.2. | 7.2.1 and 7.2.2

## Slide 14: INT NC - ENTSOG template - FGSZ-UKRTR IA
INT NC | ENTSOG template (draft) | FGSZ – UKRTRANSGAZ IA
Article 9 – Rules for allocation |  | 
1. Establish rules ensuring consistency between the allocated quantities at both sides of IP | 5.1. | Article 8: Allocation (in kWh; 25/0 oC)
2. Operating Balancing Account (OBA) | 5.2. | Artice 9: OBA IP1: ± 60 GWh; IP2: ± 10 GWh;
3: Applying OBA: NU : Nomination=allocation Aim: Value of OBA is as close to zero | 5.3. | Article 9:

## Slide 15: INT NC - ENTSOG template - FGSZ-UKRTR IA
INT NC | ENTSOG template (draft) | FGSZ – UKRTRANSGAZ IA
Article 10 – Communication procedures in case of exceptional event |  | 
1. Communication procedures in case of exceptional event | Article 6.1: oral communication in English, followed by an electronic confirmation | Article 14. a: Telephone call, after written confirmation in English
2. Inform its Network Users about relevant informations |  | Article 14. (b):”without delay inform and keep informed the other contracting party in respect of the possible impact on the quantities of gas that can be transported over the interconnection point”
a) the possible impact on the quantities and quality of gas that can be transported through the IP; | Article 6.2. the text is similar INT NC | Article 14. c:”as soon as reasonably practicable, each contracting party shall inform its respective affected network users that are active at the concerned interconnection point of the consequences for the confirmed quantities”
b) the possible impact on the confirmed quantities for network users active at the concerned IP(s); | Article 6.2. the text is similar INT NC | 
c) the expected and actual end of the exceptional event. | Article 6.2. the text is similar INT NC | Article 14 (d) once the exceptional event ends, the relevant affected contracting party(ies) shall inform the other contracting party as soon as reasonably practicable and each contracting party shall inform its respective affected NU accordingly.

## Slide 16: INT NC - ENTSOG template - FGSZ-UKRTR IA
INT NC | ENTSOG template (draft) | FGSZ – UKRTRANSGAZ IA
Article 11 – Settlement of disputes arising from Interconnection Agreements |  | 
The adjacent transmission system operators shall endeavour to solve amicably any disputes arising out of or in connection with the interconnection agreement and specify therein a dispute settlement mechanism for disputes which could not be amicably settled. |  | Article 18
The dispute settlement mechanism shall at least specify: (a) the applicable law; and |  | This IA shall be governed by German law.
(b) the court of jurisdiction |  | German Rules of International Arbitration

## Slide 17: INT NC - ENTSOG template - FGSZ-UKRTR IA
INT NC | ENTSOG template (draft) | FGSZ – UKRTRANSGAZ IA
Article 11 – Amendment process |  | 
1.The adjacent transmission system operators shall establish a transparent and detailed amendment process of their IA to be triggered by a written notice of one of the transmission system operators. |  | Article 4: each Party shall be entitled to request by written notice that the IA be amended to the new situation.
2.If the adjacent transmission system operators fail to reach an agreement on the amendment process, they may use the dispute settlement mechanisms developed in accordance with Article 11. |  | Parties shall meet to discuss in good faith

## Slide 18
IA signed on 29th of May
Test period from 01.06.2015 to 30.09.2015
The critical issues has to be practiced as
  matching process,
  backhaul issues,
  OBA
  issuing different protocols parallel with the „old” type procedures
From 01.10.2015 IA’s all stipulations will be in force.
IA entry into force

## Slide 19
Historical contracts with shipper(s) of UKT do not foresee nomination and allocation procedure
The way to get nominations from shippers with historical contract with division by shipper-pairs
Are there some regulations or other legislation that can force UKT shippers to provide necessary information to TSO?
What other mechanisms can be used by TSOs to provide all procedures at IPs?
Main challenges and open questions

## Slide 20
Thank you for your kind attention!