## Slide 1: TYNDP Capacity Calculation
Vincent Scherrer
IT Manager
Documentation
Brussels – 7th of october 2015

## Slide 2: The Basics
ENTSOG uses Capacities after Application of Lesser-Of Rule as the defining constraints when simulating its network model
Lesser-Of Rule takes the Operator Capacities as an input
  For every Point, Arc, Infrastructure Scenario, and Year, the system calculates the total of entries and exits, and then selects the minimum value
Operator Capacities are built based on
  Existing Capacity
  Increments
  System Enhancements
Two Specific Contexts
  ESW-CBA
  PS-CBA
The process is going to be explained in the following slides

## Slide 3: Context : ESW-CBA

## Slide 4: 1. Build Operator Capacities

## Slide 5: Inputs
Existing Capacity
Increments
Source : Internal Data Collection (Excel Files) from ENTSOG Members, Observers and Associated Partners
Source : Data Portal
This is the only Excel-based data collection process
Data entry with Sharepoint
Projects
Capacity Modifications

## Slide 6
TYNDP 2015
High
Existing infra
FID projects
Existing infra
FID projects
Non-FID mature projects
Existing infra
FID projects
Non-FID mature projects
Non-FID
less mature projects
Low
Mature
Existing infra
FID projects
2nd PCI list projects
non-FID
2nd PCI list
Assessment of the infrastructure gap
Basis PS-CBA
Additional assessment of ESW-CBA
Possible additional basis for PS-CBA
Feedback loop of 2nd PCI selection
Unchanged
from TYNDP 2015
Infrastructure Scenarios
High
Assessment of
ESW-CBA
Basis for PS-CBA
The calculation presented in the following slides is replicated for each infrastructure scenario.

## Slide 7: Infrastructure Scenarios
Context | Existing Capacity | Increments
FID | All | Only from FID projects
PCI | All | Only from FID projects or projects in the current legal PCI list
Mature | All | Only from Mature Projects
Non-FID | All | All

## Slide 8: Operator A

## Slide 9: 1. Initiate the Existing Capacity
Chart: 
| Y | Y+1 | Y+2 | Y+3 | Y+4 | Y+5 | ...
Existing Capacity | 10 | 10 | 10 | 10 | 10 | 10 | 10
The Existing Capacity is by definition constant over all the years covered by the TYNDP. This ensures that every change to the Operator Capacity can be traced back to a Project or a Capacity Modification.

## Slide 10: 2. Add the Increments
Chart: 
| Y | Y+1 | Y+2 | Y+3 | Y+4 | Y+5 | ...
Existing Capacity | 10 | 10 | 10 | 10 | 10 | 10 | 10
Increment 1 | 0 | 0 | 2 | 2 | 2 | 2 | 2
Increment 2 | 0 | 0 | 0 | 0 | 3 | 3 | 3
All the Increments submitted by the Promoter at this Point and in this Flow Directionare aggregated. An Increment commissioned during year Y is only considered as effective from Y+1.

## Slide 11: Operator B

## Slide 12: 1. Initiate the Existing Capacity
Chart: 
| Y | Y+1 | Y+2 | Y+3 | Y+4 | Y+5 | ...
Existing Capacity | 8 | 8 | 8 | 8 | 8 | 8 | 8

## Slide 13: 2. Add the Increments
Chart: 
| Y | Y+1 | Y+2 | Y+3 | Y+4 | Y+5 | ...
Existing Capacity | 8 | 8 | 8 | 8 | 8 | 8 | 8
Increment 1 | 0 | 3 | 3 | 3 | 3 | 3 | 3

## Slide 14: Resulting Operator Capacities

## Slide 15: Result
Chart: 
| Y | Y+1 | Y+2 | Y+3 | Y+4 | Y+5 | ...
Operator A | 10 | 10 | 12 | 13 | 16 | 16 | 16
Operator B | 8 | 11 | 15 | 15 | 15 | 15 | 15
The previous aggregation procedure produces a profile of values for each operator, that can vary from year to year, for the whole period of the TYNDP.

## Slide 16: Lesser-Of Rule Application

## Slide 17: Result
Chart: 
| Y | Y+1 | Y+2 | Y+3 | Y+4 | Y+5 | ...
Operator A | 10 | 10 | 12 | 13 | 16 | 16 | 16
Operator B | 8 | 11 | 15 | 15 | 15 | 15 | 15
Lesser-Of Rule | 8 | 10 | 12 | 13 | 15 | 15 | 15
For each year, the minimum value is then selected.

## Slide 18: Vincent Scherrer IT Manager
Vincent.scherrer@entsog.eu